Lamport's bakery algorithm

Lamport envisioned a bakery with a numbering machine at its entrance so each customer is given a unique number. Numbers increase by one as customers enter the store. A global counter displays the number of the customer that is currently being served. All other customers must wait in a queue until the baker finishes serving the current customer and the next number is displayed. When the customer is done shopping and has disposed of his or her number, the clerk increments the number, allowing the next customer to be served. That customer must draw another number from the numbering machine in order to shop again.
According to the analogy, the "customers" are threads, identified by the letter i, obtained from a global variable.
Due to the limitations of computer architecture, some parts of Lamport's analogy need slight modification. It is possible that more than one thread will get the same number n when they request it; this cannot be avoided. Therefore, it is assumed that the thread identifier i is also a priority. A lower value of i means a higher priority and threads with higher priority will enter the critical section first.

Szymański's algorithm

The algorithm
The algorithm is modeled on a waiting room with an entry and exit doorway. Initially the entry door is open and the exit door is closed. All processes which request entry into the critical section at roughly the same time enter the waiting room; the last of them closes the entry door and opens the exit door. The processes then enter the critical section one by one (or in larger groups if the critical section permits this). The last process to leave the critical section closes the exit door and reopens the entry door, so the next batch of processes may enter.
The implementation consists of each process having a flag variable which is written by that process and read by all others